## Slide 1: LAB 304 Lecture \ 3
Blood samples

## Slide 2: Learning objectives
To know how communicate with patient in order to take a sample.
To learn safety precautions of extracting blood from a vein.
To recognize the vacutainer tubes and their uses.

## Slide 3: COMMUNICATION
Most patients have had a blood extraction before.
To them the phlebotomist's statement of intending to perform a blood test is usually sufficient to understand what is about occur.
To a patient who has never had a blood test, a more detailed explanation may be necessary.
Special procedures may require additional information.

## Slide 4: COMMUNICATION
The phlebotomist must always inform the patient of the procedure and determine that the patient understands what is about to take place before proceeding.
  If a patient does not speak or understand your language, the phlebotomist may have to use sign language or other nonverbal means to demonstrate what is to occur, or an interpreter must be located.
  Speaking slowly and distinctly, using sign language or writing down information may be necessary for patients with hearing problems.

## Slide 5: COMMUNICATION
Most patients understand that the blood tests are needed in the course of their treatment.
Reminding the patient that the test was ordered by the doctor as part of their care will sometimes convince the patient to cooperate.

## Slide 6: Remember
The patient has the right to refuse the test .
When it has been determined that the patient truly refuses to cooperate, the phlebotomist should write on the requisition that the patient has refused to have blood drawn.

## Slide 7: Recommendations
Receive the patient with pleasant smile.
Gain the patient trust and confidence.
The phlebotomist should have a pleasant appearance and behave in a professional manner to convey confidence with the patient when taking blood.
In handling difficult and irritable patients, the phlebotomist should remain calm and treat the patient in a caring manner under all circumstances.
Thanking the patient for their cooperation makes them feel traumatic-free and positive about the laboratory.

## Slide 8: Procedure of blood collection
      1- Let the patient be seated on the chair comfortably.
2- Ensure the identity of the patient

## Slide 9
3- Apply a soft tubing tourniquet fastening arm band to the upper arm of the arm to enable the veins to be seen and felt. Do not apply the tourniquet too tightly or for longer than 2 minutes. Ask the patient to make a tight fist which will make the veins more prominent.
Procedure of blood collection

## Slide 10: Procedure of blood collection
4- Using the index finger, feel for a suitable vein, selecting a sufficiently large straight vein that does not roll and with a direction that can be felt.

## Slide 12: Procedure of blood collection
5- Cleanse the puncture site with 70% ethanol and allow to dry. Do not re-touch the cleansed area.

## Slide 13: Procedure of blood collection
6- With the thumb of the left hand holding down the skin below the puncture site .
7- make the venipuncture with the bevel of the needle of syringe directed upwards in the line of the vein.

## Slide 14: Procedure of blood collection
8- steadily withdraw the plunger of the syringe at the speed it is taking the vein to fill. Avoid moving the needle in the vein.
NB-If the plunger is withdrawn too quickly this can cause hemolysis of the blood and the collapse of a small vein.

## Slide 15: Procedure of blood collection
      9- When sufficient blood has been collected, release the tourniquet and instruct the patient to open his or her fist. Remove the needle and immediately press on the puncture site with a piece of dry cotton wool. Remove the tourniquet completely. Instruct the patient to continue pressing on the puncture site until the bleeding has stopped.

## Slide 16: Procedure of blood collection
10- remove the needle from the syringe, discard the needle in sharp waste container safely and carefully fill the vacutainer tube(s) with the required volume of blood .
Do not attempt to re-sheath the needle as this can result in needle-stick injury.
Important: Do not fill a container with the needle attached to the syringe. Forcing the blood through the needle can cause hemolysis .

## Slide 17: Procedure of blood collection
11- Mix immediately the blood in an EDTA, Heparin or citrate (anticoagulated) container.

## Slide 18: Procedure of blood collection
12- Check that bleeding from the venipuncture site has stopped. Cover the area with a small dressing. Putting adhesive tape is subjective- if a patient has lot of hair then it is better to keep it pressed for 5 min & check for any bleeding.

## Slide 19: Procedure of blood collection
PRECAUTION
Sometimes the patient gets a vaso-vagal attack on piercing the needle or when patient sees his blood. The phlebotomist should be experienced enough to assess such conditions, take the appropriate 1st aid e.g. laying down the patient on a flat surface with protrusion of the chin forward. Call ER for help if needed.

## Slide 20: blood collection
Vacutainer ( adapter cap ) & wings

## Slide 21: blood collection
syringe

## Slide 22: vacutainer tubes
Micro tubes

## Slide 23: Uses of vacutainer tubes
RED & YELLOW TOP
Plain (without anticoagulant)
serum
Uses :
1- all chemistry test
2- hormones
3- serology & virology

## Slide 24: Uses of vacutainer tubes
PURPLE OR LAVENDER TOP
EDTA (anticoagulant )
Plasma
Uses :
1- CBC
2- blood film
3- ABO grouping
4- malarial test
5- HA1C
6- cross matching
7- HB electrophoresis
8- sickle cell test

## Slide 25: Uses of vacutainer tubes
LIGHT BLUE TOP
SODIUM CITRATE 1:9 (anticoagulant )
Plasma
Uses :
1- PT
2- PTT
3- INR
4- D-dimer
5- FDP

## Slide 26: Uses of vacutainer tubes
GREEN TOP
HEPARIN
Plasma
Uses :
1- chemistry test
2- βHCG ( hormone )

## Slide 27: Uses of vacutainer tubes
BLACK TOP
SODIUM CITRATE 1:4
Plasma
Uses :
1- ESR

## Slide 28: Uses of vacutainer tubes
GRAY TOP
FLUORIDE & OXALATE
Plasma
Uses :
1- Glucose (especially when testing will be delayed)
2- blood alcohol

## Slide 29
All the success & prosperity
كل النجــــاح و التـــوفـــيـــق